## Slide 1: October 24, 2022
Yi Zhang
California ISO
ADS PCM Simulation Time Issue

## Slide 2: Issue
Simulation time of the 2032 ADS PCM increased significantly compared with the 2030 ADS PCM.
  Depending on computer setup, simulation time increased by almost 100%. The simulation time on the 2030 ADS PCM is about 20 hours but now the 2032 ADS PCM needs more than 40 hours when both models are simulated sequentially through the study year.

## Slide 3: Investigation
PCMS and Hitachi Energy investigated the simulation time issue.
Initial thoughts:
  Hydro weekly-model may increase computation burden for process hydro data.
  BTM PV mode with higher granularity increased number of generators.
Detailed analysis was conducted through step-by-step debugging simulation.

## Slide 4: Latest Findings
BTM PV model and weekly hydro model contribute to the simulation time increase, but not as significant as initially thought.
  Roughly contribute to about 10% of the increase.
Two largest contributors to the simulation time increase:
  Increase of the number of batteries in the model.
  Increase of the number of binding transmission constraints.

## Slide 5: Mitigation Plan
Parallel simulation with dividing the study year to multiple segments, e.g. 12 segments.
  Not always appropriate for many studies.
Work with vendor to explore and implement more efficient battery dispatch approach, and more efficient approach to process transmission constraints in economic dispatch.

## Slide 6
Yi Zhang
yzhang@caiso.com
(916) 608-5734
Bharath Kumar Ketineni
(801) 819-7654
bketineni@wecc.org